## Slide 1: C-Band for AIRBUS Telemetry : status and improvement
ETTC 2015
Gilles Freaud /Luc FALGA

## Slide 2: Airbus Telemetry context
15 aircrafts :
A380
A400M
LR ( A340 A330)
SA ( A320,A319,A321)
A350-900
9 reception antenna
Toulouse
Mediterranean see
Bordeaux
Saint-Nazaire
Tarbes
3 flights test simultaneously
4 in the next future

## Slide 3: C-Band Telemetry frequency
Allocations for telemetry (flight test purpose and only downlink) :
5091
5150
5250
RLAN (wi-fi)
Telemetry
MLS / AMRS / AS
Worldwide allocation
All primary services
FSS sharing possible
AS and AMRS sharing feasible but strong constraints on telemetry
Region 1 allocation (Europe/Africa/Brazil)
All primary services
FSS sharing possible
RLAN sharing possible but some constraints on telemetry
FSS

## Slide 4: C-Band channels for AIRBUS Telemetry
MLS / AMRS / AS / FSS
5091
5150
5250
RLAN / FSS
RLAN / FSS
5120
AMRS
Telemetry
AMRS
MLS
Worldwide: share with AS/AMRS/MLS/FSS
Europe + Africa only (Region1)
Share with RLAN & FSS
5130
5131
5139
5140
5148
5149
5157
5159
CANAL B
CANAL C
CANAL D
5120
5135
5144
5153
8 MHz
8 MHz
8 MHz
1 MHz
2 MHz
1 MHz
1 MHz
CANAL A
8 MHz
2 MHz
5122
5126

## Slide 5: Frequency for AAIRBUS telemetry
A
A320 to A318
1987 to 2004
1M
25 M
20 M
15 M
10 M
5M
A
A380 to A400M
2005 to 2012
ARINCA429
AFDX
Bi-Telemetry & data compression
A
A350-900
2013 to 2014
New data compression
2000
2014
Year
Data rate (Mbits/s
A
SA NEO
2014 to 2016
A
A350-1000
From 2016
S Band
L Band
C Band

## Slide 6: C Band achievements
Same performance compared to S-Band Telemetry :
  Quality of transmission : QEF
  Same Coverage area
  Antenna tracking
  Data repatriation from antenna to Telemetry center
Operational reliability :98,5 %
  Equal compared to S-Band Telemetry
Data rate x 2,5 :
  Answer to real need for 1st flight configuration
  Possibility to increase video quality

## Slide 7: C Band achievements
From Jan 2014 to June 2015
  943 tests followed up on C-Band
  4092 hours
  On 12 different A/Cs
TC A350 end of September 2015
SA NEO : 1st Program full C-band telemetry

## Slide 8: What’s next ?
Continuous improvement :
  Reliability
  Answer new needs (wide band parameters more than 8000 samples/s, high video quality etc …)
Support ATR for Clean Sky 2 flight test campaign
Mobile telemetry antenna
  Capacity to equip airport with reception means for specific tests follow-up :
    Paris-Vatry
    Perpignan

## Slide 9: Conclusion
A long story and a human adventure
Thanks to all the contributors !
AIRBUS was the 1st user of C-Band for Telemetry in the world
It’s now our standard : we’ll continue to improve it !

## Slide 10: Telemetry in the future ?
Airbus must have a clear vision of the future :
  Telemetry is mandatory to reach the objective of certification delay
  Managing risks and opportunities
  To anticipate regulation modification

## Slide 11
© AIRBUS Operations S.A.S. All rights reserved. Confidential and proprietary document. This document and all information contained herein is the sole property of AIRBUS Operations S.A.S. No intellectual property rights are granted by the delivery of this document or the disclosure of its content. This document shall not be reproduced or disclosed to a third party without the express written consent of AIRBUS Operations S.A.S. This document and its content shall not be used for any purpose other than that for which it is supplied. The statements made herein do not constitute an offer. They are based on the mentioned assumptions and are expressed in good faith. Where the supporting grounds for these statements are not shown, AIRBUS Operations S.A.S will be pleased to explain the basis thereof. AIRBUS, its logo, A300, A310, A318, A319, A320, A321, A330, A340, A350, A380, A400M are registered trademarks.
Protect the C-Band !